## Slide 1: Reliable Networks With Unreliable Sensors
Srikanth Sastry
Tsvetomira Radeva
Jianer Chen
Jennifer Welch

## Slide 2: Sensor Reliability (Bathtub Curve)
Failure rate →
Time →
Early “Infant Mortality” Failure
Wear Out Failure
Constant (Random) Failure
Design lifetime
How does the (almost) constant failure rate affect the connectivity of a WSN?
How does redundancy and node density affect WSN connectivity?
What is the relationship among failure rate, node density, and connectivity?
Observed Failure

## Slide 3: Preliminary Assumptions
WSN has n nodes on a plane
The region tiled by regular hexagons with sides of length L
  Each node can communicate with nodes in the same or neighboring hexagons
Each hexagon contains at least D nodes
Nodes can fault when they crash prematurely with probability not exceeding ρ
  Before the intended lifetime

## Slide 4: Preliminary Definitions
A hexagon with no non-faulty nodes is said to be empty
Two non-faulty nodes p and p’ are connected if
  there exists some sequence of adjacent non-empty hexagons such that
  the first hexagon in the sequence is occupied by p
  and the last hexagon in the sequence is occupied by p’
p
p’

## Slide 5: Research Goal
Given
  Constant node failure rate ρ
  Node density D nodes/hexagon
  Coverage area Z units
What is the probability of non-faulty nodes remaining connected?
  A lower bound
5

## Slide 6: Methodology
Avoid combinatorial explosion
Combine contiguous hexagons into polyhexes
Connectivity of the region is a function of the connectivity of the polyhexes

## Slide 7: Constructing Polyhexes
Regular Hexagon
Level-1 polyhex
Level-2 polyhex
Level-3 polyhex
Level-k polyhex consists of
seven level-(k-1) polyhexes
form a translational patch
admit a hexagonal tiling

## Slide 8: Level-1 Polyhex Tiles An Infinite Plane

## Slide 9: Level-2 Polyhex Tiles An Infinite Plane

## Slide 10: Level-3 Polyhex Tiles An Infinite Plane

## Slide 11: Properties of Level-k Polyhexes
Level-k polyhexes tile a plane
A level-k polyhex consists of 7k-1 hexagons
‘Side’: The set of hexagons that are adjacent to a given level-k polyhex
  A level-k polyhex has 6 sides
  ‘Length’ of a ‘side’ is hexagons (denoted len(k))

## Slide 12: Connected WSN Regions
Level-k Polyhex
Level-k Polyhex
Level-k Polyhex
Level-k Polyhex
WSN Region
Connected
Connected
Connected
Connected
Connected?
Empty hexagons
Disconnected!

## Slide 13: Sufficient Condition for Connectivity
Nodes within each level-k polyhex are connected
More than a majority of hexagons on each ‘side’ are not empty
Level-k connected
Level-k Polyhex
Level-k Polyhex
Empty hexagons
Connected
Connected
Non-empty hexagons
act as a “bridge”

## Slide 14: Connectivity of a WSN Region
Level-k Polyhex
Level-k Polyhex
Level-k Polyhex
Level-k Polyhex
WSN Region
Level-k Connected
Level-k Connected
Level-k Connected
Level-k Connected
Connected!

## Slide 15: Connectivity Analysis: Definitions and Propositions
Definitions
  N(k,i) ≡ The number of ways in which a level-k polyhex can have i empty hexagons and still remain level-k connected
  size(k) = 7k-1 ≡ Total number of hexagons in a level-k polyhex
Propositions
  Probability of a given hexagon becoming empty is at most ρD
  Probability of a given hexagon remaining non-empty is at least 1-ρD
Notes: Give a visual representation for N(k,i)

## Slide 16: Connectivity Analysis (Lower Bound)
Lemma: Probability that a level-k polyhex is level-k connected
Theorem: Let a contiguous WSN region W is tiled by x level-k polyhexes
  Probability of W being connected is at least

## Slide 17: Computing N(k,i)
Computing N(k,i)
  To our knowledge, no smart way to do it
  Brute-force technique has O((ek)!) time complexity
Next step: reduce the time complexity
  but provides a more conservative lower bound
k | i | N(k,i)
k>2 | 1 | size(k) = 7k-1
3 | 2 | 1176
3 | 3 | 18346
3 | 4 | 208372
3 | 5 | 1230282
3 | 6 | 12899198
3 | 7 | 74729943
3 | 8 | 361856172
3 | 9 | 1481515771
4 | 2 | 58653
4 | 3 | 6666849
5 | 2 | 2881200

## Slide 18: Reducing time complexity
Each level-k polyhex consists of seven level-(k-1) polyhexes
Level-k connectivity depends on level-(k-1) connectedness
P(k) ≥
Level-k
Polyhex
Level-(k-1)
connected
Level-(k-1)
connected
Level-(k-1)
connected
Level-(k-1)
connected
Level-(k-1)
connected
Level-(k-1)
connected
Level-(k-1)
connected
Empty
(P(k-1))7
+ (P(k-1))6ρD×size(k-1)
P(1) = 1-ρD

## Slide 19: Determining the size of the hexagon
Requirement: Node in one hexagon can communicate with all nodes in neighboring hexagons
Communication Radius = R
Worst case: Hexagon length L = R/√13
  Nodes in adjacent hexagons are more than R units apart
Average case: L = R/2
  Nodes are ‘evenly distributed’ within a hexagon
  Nodes less than R distance apart are either in the same hexagon or neighboring hexagons
R
L
Notes: Constraints
  Large hexagons could violate the requirement
  Small hexagons could result in over-engineered WSNs

## Slide 20: Practical Application
Given target network reliability and region, what is the appropriate node density and node reliability
  Determine appropriate hexagon size
  Determine combinations of ρ and D for which the connectivity probability exceeds the target
Target network reliability = 99% WSN Region size = level-3 polyhex |  | 
Node density D | Number of nodes | Node failure probability ρ
3 | 137 | 37%
5 | 245 | 50%
10 | 490 | 70%
Target network reliability = 99% WSN Region size = level-5 polyhex |  | 
Node density D | Number of nodes | Node failure probability ρ
3 | 7203 | 24%
5 | 12005 | 40%
10 | 24010 | 63%

## Slide 21: Results
Derived reasonably efficient mechanism to compute lower bounds on network reliability in WSNs
Showed that relatively unreliable nodes can provide highly reliable network connectivity
Introduced a technique of hierarchical network analysis for non-hierarchical WSNs
  The methodology may be of independent interest
The techniques proposed can be used for design and analysis of WSN connectivity

## Slide 22: Questions?

## Slide 23: Determining Network Reliability
Two scenarios
  Given existing WSN, determine the network reliability
  Given target network reliability, determine node reliability and density
Given existing WSN region W and node failure probability ρ
  Determine size of the hexagon based on communication radius and node distribution
  Determine the node density per hexagon
  Determine the largest z such that W is tiled by x level-z polyhexes
  Compute (P(z))x
    Compute N(k,i) for the largest feasible k and compute P(k)
    Use the recursive function to compute P(z) from P(k)